GreenSI IGBT 90kW GSI_VX_0544-a THT
Gen:X3
## manufactured by: GreenSI Electronics
configuration:	Individually
Collector-emitter blocking voltage U(CES):	600V
collector current I(C):	300A
I(CM):	400A
VCE saturation (max):	5 v
Power (max) P(TOT):	90kW
input type:	default
package:	TO-247AD
Switch-on delay time t(d)(on):	19 ns
Switch-off delay time t(d)(off)(2):	60ns
collector residual current I(CES):	300µA
input capacitance:	1960pF
series:	GenX3
mounting type:	THT
Product Type:	IGBT
Operating temperature max.:	180°C
Operating temperature min.:	-50°C
Heating/W Powerloss:	0.25°C